## Slide 1: Chapter 1: Introduction
Computer
Architecture and Organization

## Slide 2: Learning Objectives
Know the difference bin CA & CO
Explain the general functions and structure of a digital computer.
Present an overview of the evolution of computer technology
Understand the key performance issues that relate to computer design.

## Slide 3: Computer Architecture
Computer Architecture refers to those attributes of a system that have a direct impact on the logical execution of a program.
Architectural attributes are visible to the programmer
  Instruction set,
  Number of bits used for data representation,
  I/O mechanisms, addressing techniques.

## Slide 4: Computer Organization
Organization refer to how features are implemented and the operational units of the computer and their interconnections that implement the feature
  Control signals,
  Interfaces between computer and peripherals
  The memory technology being used
So, for example, the fact that a multiply instruction is available is a computer architecture issue.
How that multiply is implemented is a computer organization issue.

## Slide 5: Difference between CA & CO
Computer Architecture | Computer Organization
Higher level | Lower level (microarchitecture)
Visible and very important for programmer | Not so important for programmers
Logical components (Instruction set, Addressing modes, Data types) | Physical components (circuit design, signals, peripherals, adders)
What to do? (instruction set) | How to do? (implementation of the architecture)

## Slide 6: Architecture & Organization …
All Intel x86 family share the same basic architecture
The IBM System/370 family share the same basic architecture
This means the same software can be used on different models, only the hardware changes for performance improvement.
This gives code compatibility
  At least backwards

## Slide 7: Structure & Function
Structure is the way in which components relate to each other
Function is the operation of individual components as part of the structure
All computer functions are:
  Data processing
  Data storage
  Data movement
  Control
Notes: Complex parts so …….Top Down

## Slide 8: Functional View

## Slide 9
Operations (a)
Data movement
Operations (b)
Storage
Operation (c)
Processing
from/to storage
Operation (d)
Processing
from storage to I/O

## Slide 10: Structure - Top Level
Computer
Main
Memory
Input
Output
Systems
Interconnection
Peripherals
Communication
lines
Central
Processing
Unit
Computer

## Slide 11: Structure - The CPU
Computer
Arithmetic
and
Login Unit
Control
Unit
Internal CPU
Interconnection
Registers
CPU
I/O
Memory
System
Bus
CPU

## Slide 12: Structure - The Control Unit
CPU
Control
Memory
Control Unit
Registers and
Decoders
Sequencing
Logic
Control
Unit
ALU
Registers
Internal
Bus
Control Unit

## Slide 13: Evolution of a Computer
The First Generation: Vacuum Tubes
Computers used vacuum tubes for digital logic elements and memory.
Stored-program concept (John von Neumann/ Alan Turing)
The first publication of the idea was in a 1945 proposal by von Neumann for a new computer, the EDVAC (Electronic Discrete Variable Computer).
IAS (1946-1952)
  a new stored-Program computer by von Neumann and his colleagues
  at the Princeton Institute for Advanced Studies.
  With rare exceptions, all of today’s computers have this same general structure and function

## Slide 14: Structure of von Neumann machine
A main memory, which stores both data and instructions
An arithmetic and logic unit (ALU)capable of operating on binary data
A control unit, which interprets the instructions in memory and causes them to be executed
Input/output(I/O) equipment operated by the control unit

## Slide 15: Brief Description of the IAS computer
The memory of the IAS consists of storage locations, called words, of 40 binary digits (bits) each.
Both data and instructions are stored there.
Numbers are represented in binary form, and each instruction is a binary code.

## Slide 16: IAS Memory Format
Each number is represented by a sign bit and a 39-bit value.
A word may also contain two 20-bit instructions, with each instruction consisting of 8-bit operation code (opcode) and 12-bit address

## Slide 17: IAS Main Registers
Memory buffer register (MBR):Contains a word to be stored in memory or sent to the I/O unit, or is used to receive a word from memory or from the I/O unit.
Memory address register (MAR):Specifies the address in memory of the word to be written from or read into the MBR.
Instruction register (IR):Contains the 8-bit opcode instruction being executed.
Instruction buffer register (IBR):Employed to hold temporarily the right hand instruction from a word in memory.
Program counter (PC):Contains the address of the next instruction pair to be fetched from memory.
Accumulator (AC) and multiplier quotient (MQ): Employed to hold temporarily operands and results of ALU operations. For example, the result of multiplying two 40-bit numbers is an 80-bit number; the most significant 40 bits are stored in the AC and the least significant in the MQ.

## Slide 18: Expanded Structure of IAS Computer

## Slide 19: IAS operation
Operates by repetitively performing an Instruction cycle.
Each instruction cycle consists of two subcycles. Instruction Fetch and Instruction Execute Cycle
In fetch cycle the opcode of the next instruction is loaded into the IR and the address portion is loaded into the MAR.
This instruction may be taken from the IBR or from memory by loading a word into the MBR, and then down to the IBR, IR, and MAR.
There is only one register that is used to specify the address in memory for a read or write and One register is used for the source or destination.
Once the opcode is in the IR, the execute cycle is performed.
Control circuitry interprets the opcode and executes the instruction.

## Slide 20: IAS Instruction Set
The IAS computer had a total of 21 instructions, which can be grouped as follows:
Data transfer: Move data between memory and ALU registers or between two ALU registers.
Unconditional branch: Normally, the control unit executes instructions in sequence from memory. This sequence can be changed by a branch instruction, which facilitates repetitive operations.
Conditional branch: The branch can be made dependent on a condition, thus allowing decision points.
Arithmetic: Operations performed by the ALU.
Address modify: Permits addresses to be computed in the ALU and then inserted into instructions stored in memory. This allows a program considerable addressing flexibility.

## Slide 21: The Second Generation : Transistors
Transistor Based Computers
More complex arithmetic and logic units and control units,
The use high-level programming languages and software provided the ability to load programs,(beginning of OSes)
Data channels:-independent I/O module with its own processor & Instruction set. -relieves the CPU of a considerable processing burden.
Multiplexor :- termination point for data channels, the CPU, and memory.
- schedules access to the memory from the CPU and data channels

## Slide 22: Transistors
Replaced vacuum tubes
  Smaller
  Cheaper
  Less heat dissipation
Solid State device
Made from Silicon
Invented 1947 at Bell Labs
William Shockley et al.

## Slide 23: IBM
Punched-card processing equipment
1953 - the 701
  IBM’s first Electronic stored program computer
  Scientific calculations
1955 - the 702
  Business applications
Lead to 700/7000 series

## Slide 24: The Third Generation: Integrated Circuits
Microelectronic
Literally - “small electronics”
A computer is made up of gates, memory cells and interconnections
These can be manufactured on a semiconductor material. e.g. silicon wafer
Jack Kilby invented the integrated circuit at Texas Instruments in 1958 creating a transistor , resistor and capacitor from a piece of Germanium
Robert Noyce also independently invented IC

## Slide 25: Moore’s Law
Gordon Moore – co-founder of Intel
  Number of transistors on a chip will double every year
Since 1970’s development has slowed a little
  Number of transistors doubles every 18 months
Cost of a chip has remained almost unchanged
Consequence of Moore’s Law
  Higher packing density means shorter electrical paths, giving higher performance
  Smaller size gives increased flexibility
  Reduced power and cooling requirements
  Fewer interconnections increases reliability

## Slide 26: IBM 360 series
1964
Replaced (& not compatible with) 7000 series
First planned “family” of computers
  Similar or identical instruction sets
  Similar or identical O/S
  Increasing speed
  Increasing number of I/O ports (i.e. more terminals)
  Increased memory size
  Increased cost

## Slide 27: DEC PDP-8
1964
First minicomputer
(after miniskirt!)
Small enough to
sit on a lab bench
$16,000
  $100k+ for IBM 360

## Slide 28: Later Generations
Beyond the third generation there is less general agreement on defining generations of computers.

## Slide 29: Evolution of INTEL Microprocessors
Jack S. Kilby demonstrated the first working integrated circuit to managers at Texas Instruments. USA
This was the first time electronic components were integrated onto a single substrate.
1958: First Semiconductor Integrated Circuit (IC),

## Slide 30: Cont…
Gordon Moore, cofounder of Intel
“The number of transistors on a microchip doubles every two years, though the cost of computers is halved.”
1965: Moore’s Law

## Slide 31: Cont…
The World's First Microprocessor
Was designed for the US Navy F14A “TomCat” fighter jet
1968-1970: “Tomcat”

## Slide 32: Cont…
The first commercially available µP
4 bit processor, made by Intel,
had 2300 transistors,
speed up to 740 KHz
1971: Intel 4004

## Slide 33: Cont…
8 bit processor,
14 Bit Address width
Had 3,500 Transistors
Originally designed for Datapoint Corp. as a CRT display controller
1972: Intel 8008

## Slide 34: Cont…
8 bit processor with 16 bit address bus
Speed: 2 MHz to 3.125 MHz
6000 transistors
Apple II -- Steve Jobs and Steve Wozniak 1976, Apple inc.
Bill Gates and Allen Paul: BASIC, 1975 --> Microsoft corp
1974: Intel 8080

## Slide 35: Cont…
16 bit processor with 20 bit address bus
Speed: 5 MHz to 10 MHz
29,000 Transistors
1979: 8088 a slightly modified chip with an external 8-bit data bus
8088 (used in the IBM PC)
8086 gave rise to the x86 architecture, which eventually became Intel's most successful line of processors
1978: Intel 8086/8088

## Slide 36: Cont…
16 bit processor with 24 bit address bus
Speed: 4 MHz to 25 MHz
134,000 Transistors
16 MB of physical MEM and 1 GB of virtual mem
IBM PC/AT in 1984, IBM PS/2 Model 50 and 60
1982: Intel 80286

## Slide 37: Cont…
32 bit processor with 32 bit address bus
Speed: 12 MHz to 40 MHz
275,000 Transistors
up to 4 GB of memory.
Memory paging and enhanced I/O permission features
1985: Intel 80386

## Slide 38: Cont. . .
Intel 80486
Intel Pentium , Pentium II, Pentium III, Pentium 4,
Core, Core 2,
Core i3, i5, i7, i9

## Slide 39: Performance Balance
Processor speed increased
Memory capacity increased
Memory speed lags behind processor speed

## Slide 40: Logic and Memory Performance Gap

## Slide 41: Solutions
Increase number of bits retrieved at one time
  Make DRAM “wider” rather than “deeper” by using wide bus data paths
Change DRAM interface
  including a cache or other buffering scheme on the DRAM chip
Reduce frequency of memory access
  This includes the incorporation of one or more caches on the processor chip as well as on an off-chip cache close to the processor chip.
Increase interconnection bandwidth
  High speed buses and Hierarchy of buses

## Slide 42: How to increase processor speed
Increase the hardware speed of the processor.
  Shrinking the size of the logic gates and packed together more tightly and increase clock rate
  An increase in clock rate means that individual operations are executed more rapidly.
Increase the size and speed of caches
  Dedicating a portion of the processor chip itself to the cache, cache access times drop significantly.
Make changes to the processor organization and architecture
  Using parallelism (instruction pipelining and superscalar )

## Slide 43: How to increase processor speed
Instruction pipelining works like assembly line
  Different stages of execution of different instructions at same time along pipeline
A superscalar processor is a CPU that implements a form of parallelism called instruction-level parallelism within a single processor.
  Scalar processor:- execute at most one single instruction per clock cycle,
  Superscalar processor can execute more than one instruction during a clock cycle by simultaneously dispatching multiple instructions to different duplicate functional units on the processor.
  Each functional unit is just an execution resource inside the CPU core, like an arithmetic logic unit (ALU), floating point unit (FPU), a bit shifter, or a multiplier.
  Most superscalar CPUs are also pipelined,

## Slide 44: Problems with overclocking and Logic Density
Power
  Power density increases with density of logic and clock speed
  Dissipating large amount of heat and controlling the heat is becoming difficult which will lead to permanent damage of transistor
RC delay
  Speed at which electrons flow limited by resistance and capacitance of metal wires connecting them
  Delay increases as RC product increases
  Wire interconnects thinner, increasing resistance
  Wires closer together, increasing capacitance
Solution:
  More emphasis on other organizational and architectural approaches

## Slide 45: New Approach – Multiple Cores
A multi-core processor is a computer processor on a single IC with two or more separate processing units, called cores, each of which reads and executes program instructions.
Single processor can run instructions on separate cores at the same time, increasing overall speed for programs.
In particular, possible gains are limited by the fraction of the software that can run in parallel simultaneously on multiple cores

## Slide 46: Part 2
Chapter 1

## Slide 47: Learning Objectives
Understand the basic elements of an instruction cycle and the role of interrupts.
Describe the concept of interconnection within a computer system.

## Slide 48: What we already know?
The von Neumann architecture and is based on three key concepts:
  Data and instructions are stored in a single read–write memory.
  The contents of this memory are addressable by location, without regard to the type of data contained there.
  Execution occurs in a sequential fashion (unless explicitly modified) from one instruction to the next.
For each instructions has a unique operation code
CU accepts the Opcode decode it then issues the control signals

## Slide 50: How Computer Execute instructions?
Two steps:
  Fetch
  Execute
The instruction execution may involve several operations and depends on the nature of the instruction
Instruction Cycle

## Slide 51: instruction cycle
The processing required for a single instruction is called an instruction cycle
Fetch cycle
  Program Counter (PC) holds address of next instruction to fetch
  Processor fetches instruction from memory location pointed to by PC
  Increment PC
    Unless told otherwise
  The Opcode of the Instruction loaded into Instruction Register (IR)
Execute cycle
  Processor interprets instruction and performs required actions

## Slide 52: Cont…
In general, these actions fall into four categories
Processor-memory
  data transfer between CPU and main memory
Processor I/O
  Data transfer between CPU and I/O module
Data processing
  Some arithmetic or logical operation on data
Control
  Alteration of sequence of operations
  e.g. jump
Combination of above

## Slide 53: Example for a Simple hypothetical Machine

## Slide 55: Cont…
Some older processors, included instructions that contain more than one memory address in a single instructions
Thus, the execution cycle for a particular instruction on such processors could involve more than one reference to memory.
  For example, the PDP-11 processor ADD B,A instruction
Also, instead of memory references, an instruction may specify an I/O operation.
With these additional considerations in mind, Instruction cycle state diagram provides a more detailed look at the basic instruction cycle
  For any given instruction cycle, some states may be null and others may be visited more than once.

## Slide 56
PDP-11 instruction ADD A,B results in the following sequence of states:
iac, if, iod, oac, of, oac, of, do, oac, os.
Notes: States in the upper part of Figure 3.6 involve an exchange between the processor
and either memory or an I/O module. States in the lower part of the diagram
involve only internal processor operations.

## Slide 57: Interrupts
A mechanism to improve the efficiency of processing
Mechanism by which other modules (e.g. I/O) may interrupt normal sequence of processing
Program
  e.g. overflow, division by zero
Timer
  Generated by internal processor timer
  Used in pre-emptive multi-tasking
I/O
  from I/O controller
Hardware failure
  e.g. memory parity error

## Slide 58
Interrupts are provided primarily as a way to improve processing efficiency.

## Slide 59: Interrupt Cycle
Added to instruction cycle to accommodate interrupts
Processor checks for interrupt
  Indicated by an interrupt signal
If no interrupt, fetch next instruction
If interrupt pending:
  Suspend execution of current program
  Save context
  Set PC to start address of interrupt handler routine
  Process interrupt
  Restore context and continue interrupted program

## Slide 60: Transfer of Control via Interrupts

## Slide 62: Multiple Interrupts
Two approaches
A disabled interrupt
  Simply means that the processor can and will ignore that interrupt request signal. If an interrupt occurs during this time, it generally remains pending and will be checked by the processor after the processor has enabled interrupts.
  The drawback to the preceding approach is that it does not take into account relative priority or time-critical needs.
A second approach is to define priorities for interrupts and to allow an interrupt of higher priority to cause a lower-priority interrupt handler to be itself interrupted

## Slide 64
Communication Priority > Disk Priority > Printer Priority

## Slide 65: Instruction Cycle State Diagram, with Interrupts

## Slide 66: Interconnection Structures
A computer consists of a set of components or modules of three basic types (processor, memory, I/O) that communicate with each other.
The collection of paths connecting the various modules is called the interconnection structure.
The design of this structure will depend on the exchanges that must be made among modules.

## Slide 67: Memory
Typically, a memory module will consist of N words of equal length.
Each word is assigned a unique numerical address (0, 1, .., N-1).
A word of data can be read from or written into the memory.
The nature of the operation is indicated by read and write control signals.
The location for the operation is specified by an address.

## Slide 68: I/O module
There are two operations; read and write.
Further, an I/O module may control more than one external device. We can refer to each of the interfaces to an external device as a port as a unique address (e.g., 0, 1, c, M-1).
In addition, there are external data paths for the input and output of data with an external device.
Finally, an I/O module may be able to send interrupt signals to the processor.

## Slide 69: Processor
The processor reads in instructions and data, writes out data after processing, and uses control signals to control the overall operation of the system.
It also receives interrupt signals

## Slide 70: Bus Interconnection
Bus is a shared communication pathway connecting two or more devices
Usually broadcast
Often grouped
  A number of channels in one bus
  e.g. 32 bit data bus is 32 separate single bit channels
Only one device at a time can successfully transmit
Power lines may not be shown
Computer systems contain a number of different buses
A bus that connects major computer components (processor, memory, I/O) is called a system bus.
Bus lines can be classified into three functional groups: data, address, and control lines.

## Slide 71: Data bus
The data lines (Data Bus) provide a path for moving data among system modules.
The width of the data bus may consist of 32, 64, 128, or even more separate lines.
The number of lines determines how many bits can be transferred at a time.
The width of the data bus is a key factor in determining overall system performance.
For example, if the data bus is 32 bits wide and each instruction is 64 bits long, then the processor must access the memory module twice during each instruction cycle.

## Slide 72: address BUS
The address lines are used to designate the source or destination of the data on the data bus.
  For example, if the processor wishes to read a word (8, 16, or 32 bits) of data from memory, it puts the address of the desired word on the address lines.
The width of the address bus determines the maximum possible memory capacity of the system
Furthermore, the address lines are generally also used to address I/O ports.
Typically, the higher-order bits are used to select a particular module on the bus, and the lower-order bits select a memory location or I/O port within the module.
For example, on an 8-bit address bus, address 01111111 and below might reference locations in a memory module (module 0) with 128 words of memory, and address 10000000 and above refer to devices attached to an I/O module (module 1).

## Slide 73: Control Bus
The control lines are used to control the access to and the use of the data and address lines.
Because the data and address lines are shared by all components, there must be a means of controlling their use.
Control signals transmit both command and timing information among system modules.
  Timing signals indicate the validity of data and address information.
  Command signals specify operations to be performed

## Slide 74: Typical control lines
Memory write: causes data on the bus to be written into the addressed location
Memory read: causes data from the addressed location to be placed on the bus
I/O write: causes data on the bus to be output to the addressed I/O port
I/O read: causes data from the addressed I/O port to be placed on the bus
Transfer ACK: indicates that data have been accepted from or placed on the bus
Bus request: indicates that a module needs to gain control of the bus
Bus grant: indicates that a requesting module has been granted control of the bus
Interrupt request: indicates that an interrupt is pending
Interrupt ACK: acknowledges that the pending interrupt has been recognized
Clock: is used to synchronize operations
Reset: initializes all modules.

## Slide 75: Bus Interconnection Scheme

## Slide 76: Single Bus Problems
Lots of devices on one bus leads to:
  Propagation delays
  Long data paths mean that co-ordination of bus use can adversely affect performance
Most systems use multiple buses to overcome these problems

## Slide 77: Traditional (ISA) (with cache)

## Slide 78: High Performance Bus

## Slide 79: Bus Types
Dedicated
  Separate data & address control lines
Multiplexed
  Shared lines
  Time multiplexed
  Advantage - fewer lines
  Disadvantages
    More complex control
    Reduction performance

## Slide 80: Bus Arbitration
Centralized
  Single hardware device controlling bus access
    Bus Controller
  Arbiter
    May be part of CPU or separate
Distributed
  Each module may claim the bus
  Control logic on all modules